# GPLANAR3

GPLANAR3 GH-110923
Horváth György
Copyright 2007-2011, BUTE-DTMI.

# Contents

GPLANAR3	1

Contents	2

1. Introduction	4

1.1 What is GPLANAR3?	4

1.2 What is on-board?	4

1.3 Conformity	5

2. Architecture	7

2.1 Power Supply	8

2.2 Clock sources	9

2.3 MultiRate/Standard Dual SFPs	10

2.4 PCI Express x4 endpoint	11

2.5 GPON ONT Transceiver	12

2.6 DDR2 SODIMM RAM	13

2.7 Feature Connector	15

2.8 FPGA Programming	17

2.8.1 Programming through JTAG	17

2.8.2 Programming from FLASH	17

2.8.3 Partial reconfiguration	18

2.8.4 Built-in JTAG programmer	18

2.9 Status LEDs	19

3. PCB Technology	20

3.1 Overview	20

3.2 Layer stacking	20

3.3 Metric	20

3.4 Controlled impedance lines	21

3.5 MFG Files	21

3.6 Tools table	22

3.7 Apertures	22

4. FPGA test Cores	24

4.1 PCIEX4 - Endpoint Block for PCI Express v. 1.6	24

4.2 TEMAC - Virtex5 Embedded Tri-mode Ethernet MAC wrapper v. 1.3	24

4.3 DDR2 - MIG v. 2.0 generated SODIMM teszt core	25

4.4 STM16TRX - RocketIO GTP wizard v. 1.7	25

4.5 Clock domains	25

Apendix A. Schematic diagrams	26

A.1 Power supply	27

A.2 PCI Express x4	28

A.3 Multirate SFP	29

A.4 GPON ONT Transceiver	30

A.5 DDR2 SODIMM RAM	31

A.6 Feature connector and Platform FLASH	32

A.7 Unused FPGA banks	33

A.8 Decoupling and spares	34

Apendix B. Components	35

B.1 Material List	35

B.2 Component Locations	38

B2.1 Coordinate system onboard - TOP	38

B2.2 Coordinate system onboard - BOTTOM	38

B2.3 Table of component locations	39

B2.4 Insertion diagram TOP	46

B2.5 Insertion diagram BOTTOM	47

Apendix C. User Constraints File	48

# 1. Introduction

## 1.1 What is GPLANAR3?

GPLANAR3 is a PCI-Express x4 adapter card, primarily developed for emulating GPON ONTs. It's on-board resources, and reconfigurability of its FPGA extends its functionality beyond the ONT emulation.

## 1.2 What is on-board?

The figures below show the major on-board components.

Top side components:

| 1: GPON ONT Optical Subassembly (OSA) 2: Dual Gigabit Multi-Rate Multi-Standard SFP receptacle 3: DDR2 RAM SODIMM Receptacle 1.8V (Notebook RAM) 4: PCI Express x4 Edge Connector | 5: 40 pin Berg type Feature Connector 6: Xilinx Virtex-5 family FPGA device 7: Switching regulators for 1.0, 1.8, 2.5, 3.3 Volts 9: JTAG connector for programming the FPGA or Flash |
| --- | --- |

Bottom and ISA assembly side components:

| 8: Platform FLASH with initial FPGA core | 10: Interface status LED's, RED/GREEN pairs |
| --- | --- |

## 1.3 Conformity

GPLANAR3 aims the following Standards/Recommendations:

| GPON | ITU-T G.984 series Gigabit Capable Passive Optical Network |
| --- | --- |
|  | ITU-T G.984.1 General characteristics |
|  | ITU-T G.984.2 Physical Media Dependent (PMD) layer specification |
|  | ITU-T G.984.3 Transmission convergence layer specification |
| SFP | Small Formfactor Pluggable Transceivers |
|  | SFF Committee INF-8074i Specification for SFP Transceiver |
|  | SFF Committee SFF-8075 Specification for PCI Card Version of SFP Cage |
|  | SFF Committee SFF-8472 Specification for Diagnostic Monitoring Interface for Optical Xcvrs |
| ...SDH | Synchronous Digital Hierarchy |
|  | ITU-T G.707/Y.1322 Network node interface for the synchronous digital hierarchy (SDH) |
| ...GBE | Gigabit Ethernet (Optical/Copper) |
|  | IEEE Std 802.3 Carrier sense multiple access with collision detection (CSMA/CD) access method and physical layer specifications |
| PCIE | PCI Express |
|  | PCI-SIG PCI Express Base Specification Revision 1.0a |
|  | PCI-SIG PCI Express Card Electromechanical Specification Revision 1.0a |
| DDR2 | Dual DataRate II. SDRAM and Modules |
|  | JEDEC JESD79-2D DDR2 SDRAM SPECIFICATION |
|  | JEDEC No.21C 4.20.11 200-Pin DDR2 SDRAM Unbuffered SODIMM Design Specification. (Item #2017.10) Release No. 17 |
| FC | 40 pin Feature Connector |
| ...PDH | ITU-T G.703 Physical/electrical characteristics of hierarchical digital interfaces (.9 with passive feature card) |
| ...HDD | NCITS 361-2002 AT Attachment with Packet Interface - 6 (ATA/ATAPI-6/UDMA5/UDMA100/UATA100 interface) |

# 2. Architecture

The simple and robust architecture of GPLANAR3 is shown on the block diagram below.

The heart of the board is a Xilinx Virtex-5 family FPGA device.
The PCB can accomodate two types of devices:

- XC5VLX50T-1FF1136C (for GPLANAR3 board)

- XC5VLX110T-2FF1136C (for GPLANAR3X board)

The main characteristics of the devices are shown in the table below:

|  | XC5VLX50T | XC5VLX110T |
| --- | --- | --- |
| Array metric | 120x30 | 160x54 |
| Slices | 7200 | 17280 |
| LUT RAM | 480 kBytes | 1120 kBytes |
| Block RAM | 2.16 MBytes | 5.32 MBytes |
| DSP slices | 48 | 64 |
| GTP Transceivers | 12 (6 pairs) | 16 (8 pairs) |
| Clock Management Tiles | 6 | 8 |

In addition, both types have

- Clock Management Tiles (CMTs) having two Digital Clock Managers (DCM) and a Phase Locked Loop per CMT

- One PCI Express Endpoint Controller

- 4 Tri-mode (10/100/1000)Ethernet Media Access Controller (MAC)

- 2 Internal Configuration Acces Ports (ICAP)

- Core logic can run at 550MHz internal clock speed

Four GPLANAR3 models can be produced depending on the insertion of FPGA type, and the OLT transceiver as shown below:

| Model | FPGA | ONT TRX |
| --- | --- | --- |
| GPLANAR3 | XC5VLX50T | Yes |
| GPLANAR3S | XC5VLX50T | No |
| GPLANAR3X | XC5VLX110T | Yes |
| GPLANAR3SX | XC5VLX110T | No |

The following sections detail the rest of the board's architectual elements.

## 2.1 Power Supply

The figure below shows the power distribution tree for GPLANAR3.
The first stages consist of switching regulator modules (SWR), since on second stages there are low drop-out (LDO) point of load (POL) type regulators.

The signal names, nominal voltages, maximum load current, and designated targets are the following:

| Signal name | V | A | Targets | Notes |
| --- | --- | --- | --- | --- |
| VCC1 | 1.0 | 10 | FPGA | Core voltage |
| VCC1V8 | 1.8 | 10 | DDR2 RAM | Main supply |
|  | . | . | LDO Feed | for DDR2 Ref. |
|  | . | . | FPGA I/O | Bank 11,13,15,17,(19,21) |
|  | . | . | FLASH | Internal voltage |
| VCC2V5 | 2.5 | 10 | LDO Feed | For MGT LDOs |
|  | . | . | FPGA | Auxiliary voltage |
| VCC3V3 | 3.3 | 10 | SFPs | . |
|  | . | . | GPON TRX | . |
|  | . | . | FPGA I/O | Bank 20,22,1,3,0,2,4,(12,5,23,18,6,25) |
|  | . | . | Feature Conn. | for I/O std. only |
|  | . | . | FLASH/JTAG | I/O voltage |
|  | . | . | DDR2 | Supply SPD ROM |
| VCC0V9 | 0.9 | 3 | DDR2 | Reference voltage |
| AVCC1 | 1.0 | 3 | FPGA MGT | MGT's core voltage |
| AVCPLL1V2 | 1.2 | 3 | FPGA MGT | MGT's PLL supply |
| AVCTX1V2 | 1.2 | 3 | FPGA MGT | MGT's Tx/Rx Supply |

## 2.2 Clock sources

There are five clock sources available on GPLANAR3 for the FPGA cores. The following tables shows their name, nominal frequencies, designated FPGA pins, and their application.

| Signal | f [MHz] | FPGA# | Application |
| --- | --- | --- | --- |
| GERCKN * | 125.00 | H3 | SFP Gigabit Ethernet App. |
| GERCKP | (XO) | H4 | PCI Express board reference |
| PXCLKN * | 100.00 | P3 | PCI Express Hosts reference |
| PXCLKP | - | P4 | . |
| OCRCKN * | 155.52 | D4 | SFP SDH App. Reference |
| OCRCKP | (XO) | E4 | . |
| PONRCKN * | 155.52 | AL4 | GPON Reference clock |
| PONRCKP | (XO) | AL5 | . |
| GCLKN | 200.00 | L18 | System/Global Clock, and |
| GCLKP | (XO) | K17 | DDR2 reference clock |

* These clock references are routed to MGT clock pins.
XO designates LVPECL Crystal Oscillators.
  The figure below shows the MGT's clocking schematic.

## 2.3 MultiRate/Standard Dual SFPs

The GPLANAR3 board has two SFP module cages (P1,P2) that support user-installed SFP modules to support STM-1 to STM-16 (Synchronous Digital Hierarchy - SDH) and Gigabit Ethernet interfaces.

Dedicated reference clock sources are available for both standards. 125MHz for GE, and 155.52MHz for SDH.

The GPLANAR3 board provides filtered 3.3V power to both SFP modules as per the SFP specification.

Since the receptacles are routed to one MGT pair, it is mandatory to install SFP's from homogenouos technology (rates may be different). It can not mix SDH and GE appclications.

The table below lists the connectors pins and any associated FPGA connectivity. Status LED's are also listed here.

| Signal (P1) | SFP# | FPGA# |  | Signal (P2) | SFP# | FPGA# |
| --- | --- | --- | --- | --- | --- | --- |
| TXFAULT[0] | 002 | E13 |  | TXFAULT[1] | 002 | D11 |
| TXDIS[0] | 003 | G12 |  | TXDIS[1] | 003 | E11 |
| SDO[0] | 004 | E12 |  | SDO[1] | 004 | D10 |
| SCLK[0] | 005 | D12 |  | SCLK[1] | 005 | E9 |
| PLUG_N[0] | 006 | C13 |  | PLUG_N[1] | 006 | F9 |
| RATS[0] | 007 | A13 |  | RATS[1] | 007 | E8 |
| LOS[0] | 008 | B13 |  | LOS[1] | 008 | F8 |
| LEDACT_N[0] | - | G11 |  | LEDACT_N[1] | - | C12 |
| LEDLOS_N[0] | - | F11 |  | LEDLOS_N[1] | - | B12 |
| TXP[0] | 019 | B4 * |  | TXP[1] | 019 | E2 |
| TXN[0] | 018 | B3 |  | TXN[1] | 018 | D2 |
| RXP[0] | 013 | A3 |  | RXP[1] | 013 | D1 ** |
| RXN[0] | 012 | A2 |  | RXN[1] | 012 | C1 |
| GND | 001 | - |  | GND | 001 | - |
| GND | 009 | - |  | GND | 009 | - |
| GND | 010 | - |  | GND | 010 | - |
| GND | 011 | - |  | GND | 011 | - |
| GND | 014 | - |  | GND | 014 | - |
| GND | 017 | - |  | GND | 017 | - |
| GND | 020 | - |  | GND | 020 | - |
| VCC3V3 | 015 | - |  | VCC3V3 | 015 | - |
| VCC3V3 | 016 | - |  | VCC3V3 | 016 | - |

* TXPOLARITY attribute for the MGT has to be changed
** RXPOLARITY attribute for the MGT has to be changed

## 2.4 PCI Express x4 endpoint

The PCI Express endpoint connector (designated as J1 on-board) allows an FPGA design to support x1 and x4 gigabit lanes to communicate with the host, at the speed of 2.5 Gbps of each.

Caution! There is a jumper ( designated as J2 ) on board to select the proper presence detect lane configuration (close to x4) for the actual design.

The table below lists the connectors pins and any associated FPGA connectivity.

| Signal (P1) | Side A | FPGA# |  | Signal (P2) | Side B | FPGA# |
| --- | --- | --- | --- | --- | --- | --- |
| PRESENT_N | A1 | - |  | +12 VOLTS | B1 | To PWR |
| +12 VOLTS | A2 | To PWR |  | +12 VOLTS | B2 | To PWR |
| +12 VOLTS | A3 | To PWR |  | +12 VOLTS | B3 | To PWR |
| GND | A4 | - |  | GND | B4 | - |
| JTAG_TCK | A5 | - |  | SMCLK | B5 | - |
| JTAG_TDI | A6 | - |  | SMDAT | B6 | - |
| JTAG_TDO | A7 | - |  | GND | B7 | - |
| JTAG_TMS | A8 | - |  | +3.3 VOLTS | B8 | - |
| +3.3 VOLTS | A9 | - |  | JTAG_TRST_N | B9 | - |
| +3.3 VOLTS | A10 | - |  | +3.3 VAUX | B10 | - |
| PXPERST | A11 | - |  | PCIE_WAKE_N | B11 | - |
| KEY | KEY | KEY |  | KEY | KEY | KEY |
| GND | A12 | - |  | RESERVED | B12 | - |
| PXCLKP | A13 | P4 |  | GND | B13 | - |
| PXCLKN | A14 | P3 |  | PETP0 | B14 | N1 |
| GND | A15 | - |  | PETN0 | B15 | P1 |
| PERP0 | A16 | M2 |  | GND | B16 | - |
| PERN0 | A17 | N2 |  | PRESENT_N | B17 | - |
| GND | A18 | - |  | GND | B18 | - |
| RESERVED | A19 | - |  | PETP1 | B19 | R1 |
| GND | A20 | - |  | PETN1 | B20 | T1 |
| PERP1 | A21 | T2 |  | GND | B21 | - |
| PERN1 | A22 | U2 |  | GND | B22 | - |
| GND | A23 | - |  | PETP2 | B23 | W1 |
| GND | A24 | - |  | PETN2 | B24 | Y1 |
| PERP2 | A25 | V2 |  | GND | B25 | - |
| PERN2 | A26 | W2 |  | GND | B26 | - |
| GND | A27 | - |  | PETP3 | B27 | AA1 ** |
| GND | A28 | - |  | PETN3 | B28 | AB1 |
| PERP3 | A29 | AB2 * |  | GND | B29 | - |
| PERN3 | A30 | AC2 |  | --- | B30 | - |
| GND | A31 | - |  | PRESENT4_N | B31 | To J2 |
| --- | --- | - |  | GND | B32 | - |

* RXPOLARITY attribute for the MGT has to be changed
** TXPOLARITY attribute for the MGT has to be changed

Although the PCI identification codes are FPGA core dependeant, defaults are the following:

Vendor ID........ 15C6 ..... Technical University of Budapest

Device ID........ 02E3 ..... GPLANA 2.4 Gbps GPON ONU Emulator

Revision ID......    1 ..... Rev. 1. (GPLANAR3)

Base Class.......   02 ..... Network controller

Sub-Class........   80 ..... Other network controller

Interface........    0 ..... Base model, XC5VLX50T+ONT

Interface........    1 ..... Extra (X), XC5VLX110T+ONT

Interface........    2 ..... Limited (S), XC5VLX50T, no ONT

Interface........    3 ..... Limited Extra(SX), XC5VLX110T, no ONT

## 2.5 GPON ONT Transceiver

GPLANAR3 aims the emulation of multiple GPON ONUs. (Optical Network Unit). The main part of the ONU is the ONT (Optical Network Termination) transceiver - designated as P3.

ONT functions are entirelly implemented in the FPGA core. The rest of ONUs may be constructed using on-board, or host's resources. Here are some examples below:

- Two pieces of real ATM (Asynchronous Transfer Mode) interface can be implemented by plugging 155Mbps SFP transceivers into P1 and P2, with the corresponding FPGA core support

- Four real PDH interfaces can be attached to the Feature Connector (passive card required - see FC section) for ISDN PRI applications.

- Good number of 10/100Mbps Ethernet interfaces can be intruduced to the host computer, running several virtual machines (e.g. VmWare). The limit is the 8Gbps full duplex bandwidth of the PCI Ecpress x4 interface.

- Virtual endpoints of any kind can be constructed in the FPGA fabric, using the 256Mbytes RAM module to store their states and properties.

The table below summarizes the transceiver signals for ONT, and the corresponding FPGA pin numbers.

| Signal | Function | FPGA# |
| --- | --- | --- |
| RD3P * | Receive downstream | AP2 |
| RD3N | (2.48832 Gbps) | AP3 |
| TD3P ** | Burst Transmission | AN3 |
| TD3N | (1.24416 Gbps) | AN4 |
| SD3 | RX Signal Detect | AP14 |
| BEN3 | TX Burst Enable | AN14 |

* RXPOLARITY attribute for the MGT has to be changed
** TXPOLARITY attribute for the MGT has to be changed

## 2.6 DDR2 SODIMM RAM

The GPLANAR3 board contains a 200-pin, small-outline dual in-line memory module (SODIMM) receptacle ( J3 ) that supports installation of DDR2 SDRAM SODIMMs of 128MB, 256MB, or 512 MB.

Dual-rank SODIMMs may not be supported. Also, the speed grade of -1 of the default FPGA installation limits the DDR2 memory clock support to a range of 200-233MHz (400-466 million transfers per second - double rate).

A 256MB DDR2-667 SODIMM (Micron Semiconductor part number MT4HTF3264HY-667D3) is shipped with GPLANAR3 - by default.

The SODIMM interface may support customer installation of DDR2-533 and/or DDR2-400 SODIMMs too.

The table below provides a description of the memory interface signals SODIMM connector pin assignments, and the associated FPGA pin assignments.

| Signal (Front) | DIMM# | FPGA# |  | Signal (Back) | DIMM# | FPGA# |
| --- | --- | --- | --- | --- | --- | --- |
| VCC0V9 | 001 | - |  | GND | 002 | - |
| GND | 003 | - |  | DQ[4] | 004 | H29 |
| DQ[0] | 005 | L29 |  | DQ[5] | 006 | G30 |
| DQ[1] | 007 | J29 |  | GND | 008 | - |
| GND | 009 | - |  | DM[0] | 010 | H30 |
| DQS_N[0] | 011 | F29 |  | GND | 012 | - |
| DQS[0] | 013 | E29 |  | DQ[6] | 014 | F30 |
| GND | 015 | - |  | DQ[7] | 016 | G31 |
| DQ[2] | 017 | P29 |  | GND | 018 | - |
| DQ[3] | 019 | P30 |  | DQ[12] | 020 | L30 |
| GND | 021 | - |  | DQ[13] | 022 | K31 |
| DQ[8] | 023 | F31 |  | GND | 024 | - |
| DQ[9] | 025 | E31 |  | DM[1] | 026 | J31 |
| GND | 027 | - |  | GND | 028 | - |
| DQS_N[1] | 029 | N30 |  | CK[0] | 030 | B32 |
| DQS[1] | 031 | M31 |  | CK_N[0] | 032 | A33 |
| GND | 033 | - |  | GND | 034 | - |
| DQ[10] | 035 | P31 |  | DQ[14] | 036 | M30 |
| DQ[11] | 037 | R31 |  | DQ[15] | 038 | N29 |
| GND | 039 | - |  | GND | 040 | - |
| GND | 041 | - |  | GND | 042 | - |
| DQ[16] | 043 | B33 |  | DQ[20] | 044 | C34 |
| DQ[17] | 045 | C33 |  | DQ[21] | 046 | D34 |
| GND | 047 | - |  | GND | 048 | - |
| DQS_N[2] | 049 | E34 |  | NC/EVENT_N | 050 | - |
| DQS[2] | 051 | F33 |  | DM[2] | 052 | E33 |
| GND | 053 | - |  | GND | 054 | - |
| DQ[18] | 055 | F34 |  | DQ[22] | 056 | C32 |
| DQ[19] | 057 | E32 |  | DQ[23] | 058 | D32 |
| GND | 059 | - |  | GND | 060 | - |
| DQ[24] | 061 | H34 |  | DQ[28] | 062 | G33 |
| DQ[25] | 063 | H33 |  | DQ[29] | 064 | G32 |
| GND | 065 | - |  | GND | 066 | - |
| DM[3] | 067 | J34 |  | DQS_N[3] | 068 | K34 |
| NC/RESET_N | 069 | - |  | DQS[3] | 070 | L34 |
| GND | 071 | - |  | GND | 072 | - |
| DQ[26] | 073 | K32 |  | DQ[30] | 074 | J32 |
| DQ[27] | 075 | L33 |  | DQ[31] | 076 | K33 |
| GND | 077 | - |  | GND | 078 | - |
| CKE[0] | 079 | N32 |  | CKE[1] | 080 | M32 |
| VCC1V8 | 081 | - |  | VCC1V8 | 082 | - |
| NC/CSN[2] | 083 | - |  | A[15] | 084 | R32 |
| BA[2] | 085 | P32 |  | A[14] | 086 | R33 |
| VCC1V8 | 087 | - |  | VCC1V8 | 088 | - |
| A[12] | 089 | U31 |  | A[11] | 090 | T33 |
| A[9] | 091 | P34 |  | A[7] | 092 | U32 |
| A[8] | 093 | V25 |  | A[6] | 094 | U33 |
| VCC1V8 | 095 | - |  | VCC1V8 | 096 | - |
| A[5] | 097 | W29 |  | A[4] | 098 | Y28 |
| A[3] | 099 | R34 |  | A[2] | 100 | V29 |
| A[1] | 101 | V24 |  | A[0] | 102 | AA30 |
| VCC1V8 | 103 | - |  | VCC1V8 | 104 | - |
| A[10] | 105 | W26 |  | BA[1] | 106 | W31 |
| BA[0] | 107 | V27 |  | RAS_N | 108 | AA31 |
| WE_N | 109 | V28 |  | CS_N[0] | 110 | Y31 |
| VCC1V8 | 111 | - |  | VCC1V8 | 112 | - |
| CAS_N | 113 | Y29 |  | ODT[0] | 114 | T34 |
| CS_N[1] | 115 | AA29 |  | A[13] | 116 | AB31 |
| VCC1V8 | 117 | - |  | VCC1V8 | 118 | - |
| ODT[1] | 119 | V30 |  | NC/CSN[3] | 120 | - |
| GND | 121 | - |  | GND | 122 | - |
| DQ[32] | 123 | V32 |  | DQ[36] | 124 | Y33 |
| DQ[33] | 125 | V33 |  | DQ[37] | 126 | Y32 |
| GND | 127 | - |  | GND | 128 | - |
| DQS_N[4] | 129 | V34 |  | DM[4] | 130 | AB32 |
| DQS[4] | 131 | W34 |  | GND | 132 | - |
| GND | 133 | - |  | DQ[38] | 134 | Y34 |
| DQ[34] | 135 | AA33 |  | DQ[39] | 136 | AA34 |
| DQ[35] | 137 | AB33 |  | GND | 138 | - |
| GND | 139 | - |  | DQ[44] | 140 | AD32 |
| DQ[40] | 141 | AC32 |  | DQ[45] | 142 | AK32 |
| DQ[41] | 143 | AC33 |  | GND | 144 | - |
| GND | 145 | - |  | DQS_N[5] | 146 | AD34 |
| DM[5] | 147 | AE33 |  | DQS[5] | 148 | AC34 |
| GND | 149 | - |  | GND | 150 | - |
| DQ[42] | 151 | AE32 |  | DQ[46] | 152 | AF33 |
| DQ[43] | 153 | AE34 |  | DQ[47] | 154 | AF34 |
| GND | 155 | - |  | GND | 156 | - |
| DQ[48] | 157 | AH34 |  | DQ[52] | 158 | AM33 |
| DQ[49] | 159 | AJ34 |  | DQ[53] | 160 | AK34 |
| GND | 161 | - |  | GND | 162 | - |
| NC/TEST | 163 | - |  | CK[1] | 164 | AN34 |
| GND | 165 | - |  | CK_N[1] | 166 | AN33 |
| DQS_N[6] | 167 | AL33 |  | GND | 168 | - |
| DQS[6] | 169 | AL34 |  | DM[6] | 170 | AN32 |
| GND | 171 | - |  | GND | 172 | - |
| DQ[50] | 173 | AK33 |  | DQ[54] | 174 | AP32 |
| DQ[51] | 175 | AJ32 |  | DQ[55] | 176 | AM32 |
| GND | 177 | - |  | GND | 178 | - |
| DQ[56] | 179 | AF31 |  | DQ[60] | 180 | AK31 |
| DQ[57] | 181 | AG30 |  | DQ[61] | 182 | AD30 |
| GND | 183 | - |  | GND | 184 | - |
| DM[7] | 185 | AF30 |  | DQS_N[7] | 186 | AH30 |
| GND | 187 | - |  | DQS[7] | 188 | AJ30 |
| DQ[58] | 189 | AD29 |  | GND | 190 | - |
| DQ[59] | 191 | AE29 |  | DQ[62] | 192 | AH29 |
| GND | 193 | - |  | DQ[63] | 194 | AF29 |
| SDA | 195 | AH19 |  | GND | 196 | - |
| SCL | 197 | AF19 |  | SA0 | 198 | (GND) |
| VCC3V3 | 199 | - |  | SA1 | 200 | (GND) |

## 2.7 Feature Connector

Mainly for historical reason, a 40 pins BERG type Feature Connector ( designated as J5 ) is used for GPLANAR3.

The table below shows the pinout assignment for FPGA cores implementing IDE/HDD applications.

| Signal (even) | J5# | FPGA# | . | Signal (odd) | J5# | FPGA# |
| --- | --- | --- | --- | --- | --- | --- |
| FRST | 01 | H14 |  | GND | 02 | - |
| FD[7] | 03 | J14 |  | FD[8] | 04 | H20 |
| FD[6] | 05 | K14 |  | FD[9] | 06 | J20 |
| FD[5] | 07 | L14 |  | FD[10] | 08 | L20 |
| FD[4] | 09 | G15 |  | FD[11] | 10 | J21 |
| FD[3] | 11 | H15 |  | FD[12] | 12 | K21 |
| FD[2] | 13 | J15 |  | FD[13] | 14 | L21 |
| FD[1] | 15 | L15 |  | FD[14] | 16 | G22 |
| FD[0] | 17 | G16 |  | FD[15] | 18 | H22 |
| GND | 19 | - |  | FKEY | 20 | J22 |
| FDRQ | 21 | J16 |  | GND | 22 | - |
| FIOWN | 23 | K16 |  | GND | 24 | - |
| FIORN | 25 | L16 |  | GND | 26 | - |
| FIORDY | 27 | H17 |  | FBALE | 28 | K22 |
| FDACKN | 29 | J17 |  | GND | 30 | - |
| FIRQ | 31 | H18 |  | FIOCSN | 32 | G23 |
| FA[1] | 33 | K18 |  | GND | 34 | - |
| FA[0] | 35 | H19 |  | FA[2] | 36 | H23 |
| FCSN[0] | 37 | J19 |  | FCSN[1] | 38 | L19 |
| FACT | 39 | K19 |  | GND | 40 | - |

For PDH applications, a passive child board (type D1558001-LIU) has to be connected to J5. The pinout can be found in the table below.

| Signal (even) | J5# | FPGA# | . | Signal (odd) | J5# | FPGA# |
| --- | --- | --- | --- | --- | --- | --- |
| NC | 01 | H14 |  | GND | 02 | - |
| TTXA[0] | 03 | J14 |  | TTXB[0] | 04 | H20 |
| RTXA[0] | 05 | K14 |  | TTXB[0] | 06 | J20 |
| TTXA[1] | 07 | L14 |  | TTXA[1] | 08 | L20 |
| RTXA[1] | 09 | G15 |  | RTXA[1] | 10 | J21 |
| TTXA[2] | 11 | H15 |  | TTXA[2] | 12 | K21 |
| RTXA[2] | 13 | J15 |  | RTXA[2] | 14 | L21 |
| TTXA[3] | 15 | L15 |  | TTXA[3] | 16 | G22 |
| RTXA[3] | 17 | G16 |  | RTXA[3] | 18 | H22 |
| GND | 19 | - |  | NC | 20 | J22 |
| TRX[0] | 21 | J16 |  | GND | 22 | - |
| NC | 23 | K16 |  | GND | 24 | - |
| RRX[0] | 25 | L16 |  | GND | 26 | - |
| NC | 27 | H17 |  | NC | 28 | K22 |
| RRX[1] | 29 | J17 |  | GND | 30 | - |
| TRX[1] | 31 | H18 |  | NC | 32 | G23 |
| TRX[2] | 33 | K18 |  | GND | 34 | - |
| RRX[2] | 35 | H19 |  | NC | 36 | H23 |
| TRX[3] | 37 | J19 |  | NC | 38 | L19 |
| RRX[3] | 39 | K19 |  | GND | 40 | - |

TTX signals drives the TIP side pulses, RTX signals drives RING.
RRX and TRX signals carry received pulses (RING and TIP).

Note that TTXA and TTXB signals are bound together on the child board to achive the 3 volts peak voltage of the transmitted pulses. (conforming ITU-T Rec. G.703) Crosscurrent glitches are limited by serial resistors on GPLANAR3 card.

The child board has four interfaces with RJ12 connectors, as shown below.

## 2.8 FPGA Programming

Three configuration methods are available on GPLANAR3 to upload (program) the FPGA core.

### 2.8.1 Programming through JTAG

FPGA core can be loaded directly through the JTAG port (designated as J7 on-board) as shown in the figure below

### 2.8.2 Programming from FLASH

From the Platform FLASH (designated as U11), the FPGA can be loaded automatically.
If J4 jumper is open - it happens one time during the power-up.
If J4 is closed, every fundamental reset causes reconfiguration of the FPGA from the Platform FLASH.
The FLASH itself has to be burned through the JTAG with a valid configuration stream.

### 2.8.3 Partial reconfiguration

If the Platform FLASH contains the proper core implementing a PCI Express endpoint, and a controller core for ICAP (Internal Configuration Access Port) - this RESIDENT core allows the Partial reconfiguration of the FPGA.
TRANSIENT cores can be loaded that way.

J6 jumper controls HSWAPEN.

### 2.8.4 Built-in JTAG programmer

An internal JTAG programmer can be implemented in the FPGA. The pinout for the internal programmer:

| J11# | Signal | FPGA# |
| --- | --- | --- |
| 1 | ITCK | AG15 |
| 2 | ITDO | AG16 |
| 3 | ITDI | AH17 |
| 4 | ITMS | AG17 |

J7 can be used as a normal JTAG connector. If the jumper block installed, the internal controller can be used to program the FLASH.

## 2.9 Status LEDs

There are two status LEDs assigned to an interface on board.
One red colored LOS (Loss of Signal) and one green colored ACT (Activity). The table below summarizes the assignment:

| Signal | LED | Interface | FPGA# |
| --- | --- | --- | --- |
| LEDACT_N[0] | Green | SFP1 | G11 |
| LEDLOS_N[0] | Red | SFP1 | F11 |
| LEDACT_N[1] | Green | SFP2 | C12 |
| LEDLOS_N[1] | Red | SFP2 | B12 |
| LEDACT_N[2] | Green | GPON | F13 |
| LEDLOS_N[2] | Red | GPON | G13 |

# 3. PCB Technology

## 3.1 Overview

GPLANAR3 lays on a six layered FR4 PCB with SMD components on both sides, and gold plated edge connector. Through hole, and heavier componets are inserted on top.

Its form factor conforms the PCI Express x4 Full Height, Half Length Add-in Card with an I/O Bracket.

The following chapters describe the layer stacking, the metric of routing/plane copper layer, etc...

## 3.2 Layer stacking

The table below shows the layer structure of the board, and the names of the corresponding GERBER files.

| 1 | 17.5 um Cu | GPLANAR3_L1_TOP.gbr |
| --- | --- | --- |
|  | 2x100 um prepreg | - |
| 2 | 35 um Cu | GPLANAR3_L2_GND.gbr |
|  | 350 um Core | - |
| 3 | 35 um Cu | GPLANAR3_L3_MID1.gbr |
|  | 2x100 um prepreg | - |
| 4 | 35 um Cu | GPLANAR3_L4_VCC.gbr |
|  | 350 um Core | - |
| 5 | 35 um Cu | GPLANAR3_L5_MID2.gbr |
|  | 2x100 um prepreg | - |
| 6 | 17.5 um Cu | GPLANAR3_L6_BOT.gbr |

## 3.3 Metric

The narrowest traces are 6 (six) mils wide. The clearence (TT,TP) is 6 (six) mils.

Via's are all 'through' types, and covered by solder mask coating on both sides. All potential test points are available on SMD pads.

The Solder Mask Annual Ring is 2 mils (for Non-Solder-Mask-Defined pads too).

Smallest vias are 20/10 mils. All plane connections are direct type, for better cooling and conducting performance.

## 3.4 Controlled impedance lines

There are several lines used to carry very high speed data. Sigle ended lines have 50 ohm nominal impedance. Differential lines are 100 ohms. The table below shows the metric of the lines for the layer stacking above.

| Layers | Type | Metric | Zo |
| --- | --- | --- | --- |
| 1,6* | Coated surface uStrip | 12 mils single trace | 53.8 |
| 1,6* | Differential, edge coupled Coated surface uStrip | 8 mils trace-pair, 7 mils gap | 103 |
| 1,6* | Differential, Coplanar Waveguide with Ground | 8 mils trace-pair, 7 mils gap, GND edge at 6 mils | 99 |
| 3,5** | Offset Stripline | 6 mils single trace | 54 |
| 3,5** | Differential, edge coupled Offset Stripline | 6 mils trace pair, 10 mils gap | 98 |

* Layer 6 has grounded/filled polygons on Layer 5 for controlled impedance lines.

** Layer 5 has grounded/filled polygons on Layer 6 for controlled impedance lines.

## 3.5 MFG Files

PCB file(s)

~~~~~~~~~~~

GPLANAR3.PCB ..................... Tango 2 (DOS) Format

Aperture and NC Files

~~~~~~~~~~~~~~~~~~~~~~

GPLANAR3_TANGO_APERTURES.rep ..... Aperture+tool report (Tango)

GPLANAR3_DRILL.ncd ............... NC Drill

GPLANAR3_DRILL.gbr ............... Gerber Drill Holes

Layers (GERBER)

~~~~~~~~~~~~~~~~~~~~

From top to bottom:

GPLANAR3_PASTE_TOP.gbr ........... Solder Paste, TOP

GPLANAR3_SILK_TOP.gbr ............ Silk+Boardout, TOP

GPLANAR3_MASK_TOP.gbr ............ Solder Mask+Boardout, TOP

GPLANAR3_L1_TOP.gbr .............. Top routing layer

GPLANAR3_L2_GND.gbr .............. Ground Plane

GPLANAR3_L3_MID1.gbr ............. MID1 routing layer

GPLANAR3_L4_VCC.gbr .............. Power Plane with Islands (VCCx)

GPLANAR3_L5_MID2.gbr ............. MID2 routing+Plane (GND/VCCx)

GPLANAR3_L6_BOT.gbr .............. Bottom routing++Plane (GND)

GPLANAR3_MASK_BOT.gbr ............ Solder Mask+Boardout, BOTTOM

GPLANAR3_SILK_BOT.gbr ............ Silk+Boardout, TOP

GPLANAR3_PASTE_BOT.gbr ........... Solder Mask+Boardout, BOTTOM

Other files

~~~~~~~~~~~~~~~~~~~~~~

GPLANAR3.gwk ..................... GC-PREVUE job file

GPLANAR3_COMBI_LOC.txt ........... Combined Component Locations

GPLANAR3_MATERIALS.txt ........... Material List (Tango)

GPLANAR3_TANGO_LOC.rep ........... Component Locations (Tango)

GPLANAR3_TANGO_CMP.rep ........... Component List (Tango)

## 3.6 Tools table

+-----+------+

|Tool | Dia. |

|Code | mils |

+=====+======+

|T01  |  10  |

|T02  |  12  |

|T03  |  30  |

|T04  |  32  |

|T05  |  38  |

|T06  |  42  |

|T07  |  46  |

|T08  |  55  |

|T09  |  62  |

|T010 |  64  |

|T011 | 125  |

|T012 | 130  |

+-----+------+

## 3.7 Apertures

D Code Shape    X    Y

-------------------------

D10    Ellipse  004  004   Flash/Draw

D11    Ellipse  006  006    .

D12    Ellipse  008  008    .

D13    Ellipse  010  010    .

D14    Ellipse  012  012    .

D15    Ellipse  014  014

D16    Ellipse  020  020

D17    Ellipse  024  024

D18    Ellipse  040  040

-------------------------

D19    Ellipse  032  032   Flash

D20    Ellipse  028  028    .

D21    Ellipse  050  050    .

D22    Ellipse  052  052    .

D23    Ellipse  054  054    .

D24    Ellipse  060  060

D25    Ellipse  064  064

D26    Ellipse  058  058

D27    Ellipse  062  062

D28    Ellipse  066  066

D29    Ellipse  090  090

D30    Ellipse  075  075

D31    Ellipse  094  094

D32    Ellipse  200  200

D33    Ellipse  150  150

D34    Ellipse  204  204

D35    Ellipse  274  274

D36    Ellipse  145  145

D37    Ellipse  278  278

D38    Ellipse  082  082

D39    Ellipse  084  084

D40    Oval     012  036

D41    Oval     016  040

D42    Oval     036  012

D43    Oval     040  016

D44    Rd Rect  026  180

D45    Rd Rect  030  184

D46    Rd Rect  120  240

D47    Rd Rect  124  244

D48    Sq Rect  014  078

D49    Sq Rect  018  082

D50    Sq Rect  020  024

D51    Sq Rect  024  028

D52    Sq Rect  022  030

D53    Sq Rect  026  034

D54    Sq Rect  024  020

D55    Sq Rect  028  024

D56    Sq Rect  030  036

D57    Sq Rect  034  040

D58    Sq Rect  036  030

D59    Sq Rect  040  034

D60    Sq Rect  042  042

D61    Sq Rect  046  046

D62    Sq Rect  050  050

D63    Sq Rect  054  054

D64    Sq Rect  050  052

D65    Sq Rect  054  056

D66    Sq Rect  052  050

D67    Sq Rect  056  054

D68    Sq Rect  052  064

D69    Sq Rect  056  068

D70    Sq Rect  060  060

D71    Sq Rect  064  064

D72    Sq Rect  060  078

D73    Sq Rect  064  082

D74    Sq Rect  062  012

D75    Sq Rect  066  016

D76    Sq Rect  062  076

D77    Sq Rect  066  080

D78    Sq Rect  064  052

D79    Sq Rect  068  056

D80    Sq Rect  070  070

D81    Sq Rect  074  074

D82    Sq Rect  076  062

D83    Sq Rect  080  066

D84    Sq Rect  078  020

D85    Sq Rect  082  024

D86    Sq Rect  078  060

D87    Sq Rect  082  064

D88    Sq Rect  090  090

D89    Sq Rect  094  094

D90    Sq Rect  100  106

D91    Sq Rect  104  110

D92    Sq Rect  106  100

D93    Sq Rect  110  104

D94    Sq Rect  180  180

D95    Sq Rect  184  184

D96    Ellipse  030  030

# 4. FPGA test Cores

The on-board subsystems have been successfully tested using the Xilinx's Coregen generated cores. User Constraints files were modified according to the boards metric. Further modifications are discussed below on a per-Core bases.

These test Cores are available in the Distribution media:

## 4.1 PCIEX4 - Endpoint Block for PCI Express v. 1.6

This core implements a PCI Express x4 endpoint, with a completer allowing R/W access to the on-chip RAM block.

Little modifications were made to the orignal top level design. Red LED's above P1, P2, and P3 signal failures.
P1 - PLLLKDET lit if the GTP's PLL is not locked.
P2 - LINKUP lit if link training have failed for the lanes.
P3 - CLKLOCK lit if the on-chip PLL_ADV did not locked.

In order to report the presence of all four lanes, J2 has to be closed. Closing J4 forces the FPGA to be reloaded from the Platform Flash when the OS restarts, or the reset button is pushed on the PC.

Using the Microsoft Windows XP operating system, GPLANAR3 is found as a new hardware with the following ID's:

Vendor:     15C6 - BUTE

Device:     02E3 - 2.4 Gbps GPON ONU Emulator

Revision:      1

Base Class:   02 - Network

Subclass:     80 - Other

## 4.2 TEMAC - Virtex5 Embedded Tri-mode Ethernet MAC wrapper v. 1.3

The dual-SFP subystems have been successfully tested using the Xilinx's TEMAC core. The example design Autonegotiates with the other party, and send back every ethernet frames with the SRC and DST addresses swapped.

Our test suite consists of a Cisco Catalyst 3500 XL having a GBIC optical module type D-Link DGS-707, and a GPLANAR3 board having a SFP optical module type D-Link DEM-311GT.
Both P1 and P2 receptacle were tested successfully.

Little modifications were made to the orignal top level design.
In temac.vhd the EMAC0_PHYINIT_AUTONEG_ENABLE and EMAC1_PHYINIT_AUTONEG_ENABLE were set to TRUE. Also the GTP's TX/RX POLARITY were changed - reflecting the boards routing strategy. Red LED's above P1, P2, and P3 signal failures.
P1 - EMAC0CLIENTSYNCACQSTATUS lit if failed to acquired the synchron.
P2 - EMAC1CLIENTSYNCACQSTATUS lit if failed to acquired the synchron.

Green LED's above P1, P2, and P3 acts as described below.
P1 - LOS lit if signal present. (no Losss Of Signal)
P2 - LOS lit if signal present. (no Losss Of Signal)
P3 - testcnb(26) Blinks slowly if 200 MHz global clock is OK. This signal is not related to the TEMAC core, it is just for testing.

The test is passed if the interface status LED of the switch is green (link is up), and GPLANAR3 shows green lit for all LEDs (P3 blinks slowly).

## 4.3 DDR2 - MIG v. 2.0 generated SODIMM teszt core

GPLANAR3 has a 256 MBytes DDR2-400 SODIMM type MT4HTF3264HY-667 installed by default. The Memory Interface Generator produced a test core that initialize the module, and performs continuous R/W tests.

Little modifications were made to the orignal top level design.
Red LED's above P1 signals failure.
P1 - phy_init_done lit if failed to initialize the module.

Green LED's above P1, P2 acts as described below.
P1 - error lit if the R/W test does not reveal bit errors. This signal is latched. Close pin 1 and 20 on the feature connector to reset the core in order to restart the test.
P2 - testcnt(26) Blinks slowly if 200 MHz global clock is OK.

The test is passed if GPLANAR3 shows green lit for all LEDs (P2 blinks slowly).

## 4.4 STM16TRX - RocketIO GTP wizard v. 1.7

Although the GPON SFF transceiver has no stand-alone test core (yet), STM16TRX core tests the involved GTP tile in serial PMA loopback mode.

The GTP wizard generated example design contains a SDH/SONET like frame generator, and a frame checker (payload inclusive).

Some modifications were made to the orignal top level design example_mgt_top.vhd, and to the frame checker frame_check.vhd.

The error counts from the transceivers were wired out to the feature connector. GTP0 errors to FD(0..7) since GTP1 to FD(8..15). Note that GTP0 in this tile is not connected, since GTP1 is connected to the GPON ONT transceiver,

Red LED's above P1, P2, and P3 functions:
P1 - framesync0 lit if the frame checker 0 can not acquire the frame synchron.
P2 - framesync1 lit if the frame checker 1 can not acquire the frame synchron.
P3 - testcnt(26) blinks slowly if TX clock is OK.

Green LED's above P1, P2, and P3 acts as described below.
P1 - errorlat0 lit if no bit error has occured yet during the frame check
P2 - errorlat1 lit if no bit error has occured yet during the frame check
P3 - testcnb(26) blinks slowly if RX recovered clock is OK.

The test is passed if GPLANAR3 shows green lit P1,P2, and P3 LEDs blink slowly.

## 4.5 Clock domains

The following table summarizes the proposed clock domains to help devloping new/combined FPGA Cores.

It can also be used for estimating the performace of core by using the data bits column for a given clock rate.

| Signal | f [MHz] | FPGA Res. | Core | D bits | Source |
| --- | --- | --- | --- | --- | --- |
| core_clk | 250.00 | 1 PLL_ADV | pciex4 | n.a. | Slot clock (100MHz) |
| user_clk | 125.00 | see above | pciex4 | 64 | Slot clock (100MHz) |
| clk200 | 200.00 | see below | ddr2 | n.a. | Crystal Osc. X4 |
| clk0 | 200.00 | 1 DCM_ADV | ddr2 | 128 | Crystal Osc. X4 |
| clk90 | 200.00 | see above | ddr2 | n.a. | Crystal Osc. X4 |
| clkdiv0 | 100.00 | see above | ddr2 | Cal. | Crystal Osc. X4 |
| clk125 | 125.00 | n.a. | temac | 8 | Crystal Osc. X1 |
| tilem_rxrecclkn_i * | 311.04 | n.a. | stm16trx | to DCM below | RX recovered clock |
| tilem_rxusrclkn_i | 311.04 | 1 DCM_ADV | stm16trx | 8 (in GTP) | RX recovered clock |
| tilem_rxusrclk2n_i | 155.52 | see above | stm16trx | 16 | RX recovered clock |
| tilem_txusrclkn_i | 311.04 | 1 PLL_ADV | stm16trx | 8 (in GTP) | Crystal Osc. X2 or X3 |
| tilem_txusrclk2n_i | 155.52 | see above | stm16trx | 16 | Crystal Osc. X2 or X3 |

* SFPs occupy Tile m=5 GTP n=0 and 1
   GPON occupies Tile m=0 GTP n=1, n=0 is not used
   Also note that only 8 data bits, and loop clocking are used for GPON ONT transmission.

# Apendix A. Schematic diagrams

## A.1 Power supply

## A.2 PCI Express x4

## A.3 Multirate SFP

## A.4 GPON ONT Transceiver

## A.5 DDR2 SODIMM RAM

## A.6 Feature connector and Platform FLASH

## A.7 Unused FPGA banks

## A.8 Decoupling and spares

# Apendix B. Components

## B.1 Material List

QTY| TYPE       |Value    |RefDes                  |Supplier

---+------------+---------+------------------------+---------

6|CESMT       |1000u    |C10,C11,C21,C31,C32,C42 |Mouser

|E7343       |         |                        |

|            |         |                        |

7|CESMT       |10u      |C116,C117,C128,C129,    |Farago

|A3216       |         |C140,C86,C99            |

|            |         |                        |

4|CESMT       |220u     |C16,C29,C40,C8          |Mouser

|E7343       |         |                        |

|            |         |                        |

23|CSMT        |10u      |C1,C12,C13,C142,C157,   |Mouser

|C0603       |         |C169,C17,C18,C19,C2,C22,|

|            |         |C23,C26,C27,C28,C33,C34,|

|            |         |C37,C38,C39,C5,C6,C7    |

|            |         |                        |

120|CSMT        |47n      |C100,C102,C107,C108,    |In stock

|C0402       |         |C109,C110,C111,C112,    |

|            |         |C115,C118,C119,C120,    |

|            |         |C121,C122,C123,C124,    |

|            |         |C125,C126,C127,C130,    |

|            |         |C131,C133,C134,C135,    |

|            |         |C136,C138,C139,C143,    |

|            |         |C144,C145,C146,C147,    |

|            |         |C148,C149,C150,C151,    |

|            |         |C152,C153,C154,C158,    |

|            |         |C159,C160,C161,C162,    |

|            |         |C163,C164,C165,C166,    |

|            |         |C167,C168,C170,C171,    |

|            |         |C172,C173,C174,C175,    |

|            |         |C176,C177,C178,C179,    |

|            |         |C180,C181,C182,C183,    |

|            |         |C184,C185,C43,C44,C45,  |

|            |         |C46,C47,C48,C50,C51,C53,|

|            |         |C55,C56,C58,C60,C62,C64,|

|            |         |C65,C67,C69,C70,C72,C73,|

|            |         |C74,C75,C76,C77,C82,C84,|

|            |         |C87,C88,C89,C90,C91,C92,|

|            |         |C94,C95,C96,C97,C98,    |

|            |         |C104,C105,C49,C52,C54,  |

|            |         |C57,C59,C61,C63,C66,C68,|

|            |         |C71,C78,C79,C80,C81     |

|            |         |                        |

|            |         |                        |

6|CSMT        |470p     |C101,C103,C113,C114,C83,|In stock

|C0603       |         |C85                     |

|            |         |                        |

13|CSMT        |100n     |C132,C137,C14,C141,C15, |In stock

|C0603       |         |C155,C156,C24,C25,C3,   |

|            |         |C35,C36,C4              |

|            |         |                        |

4|CSMT        |1n       |C20,C30,C41,C9          |Farago

|C0603       |         |                        |

|            |         |                        |

1|DDR2-SODIMM |         |J3                      |Mouser

|SODIM200    |         |                        |

|            |         |                        |

3|DLED        |3mm      |D1,D2,D3                |Farago

|D2LED100    |Red+Green|                        |

|            |         |                        |

1|FEACON      |         |J5                      |In stock

|FEACON      |         |                        |

|            |         |                        |

1|JTAGCON     |VAL      |J7                      |In stock

|JTAGCON     |         |                        |

|            |         |                        |

39|LSMD        |220      |L1,L10,L11,L12,L13,L14, |Mouser

|L0603       |         |L15,L16,L17,L18,L19,L2, |

|            |         |L20,L21,L22,L23,L24,L25,|

|            |         |L26,L27,L28,L29,L3,L30, |

|            |         |L31,L32,L33,L34,L35,L36,|

|            |         |L37,L38,L39,L4,L5,L6,L7,|

|            |         |L8,L9                   |

|            |         |                        |

1|NU-73B94B-P |         |P3                      |In stock

|SFF2X5PIG   |         |                        |

|            |         |                        |

1|OSC         |125.00MHz|X1                      |Mouser

|XO5X7       |         |                        |

|            |         |                        |

2|OSC         |155.52MHz|X2,X3                   |Mouser

|XO5X7       |         |                        |

|            |         |                        |

1|OSC         |200.00MHz|X4                      |Mouser

|XO5X7       |         |                        |

|            |         |                        |

1|PCIEX4M     |         |J1                      |PCB contsr.

|PCIEX4M     |         |                        |

|            |         |                        |

3|PIN2        |VAL      |J2,J4,J6                |In stock

|PIN2        |         |                        |

|            |         |                        |

4|PTH08T220W  |         |U2,U4,U6,U8             |Mouser

|DIP-EBS     |         |                        |

|            |         |                        |

8|RN4X        |22       |RN1,RN2,RN3,RN4,RN5,RN6,|Farago

|RN1206X     |         |RN7,RN8                 |

|            |         |                        |

2|RSMT        |0        |R1,R14                  |Farago

|R0805       |         |                        |

|            |         |                        |

2|RSMT        |1k8      |R10,R16                 |Farago

|R0805       |         |                        |

|            |         |                        |

97|RSMT        |51       |R100,R101,R102,R103,    |In stock

|R0402       |         |R104,R105,R106,R107,    |

|            |         |R108,R109,R110,R111,    |

|            |         |R112,R113,R114,R115,    |

|            |         |R116,R117,R118,R119,    |

|            |         |R120,R121,R122,R123,    |

|            |         |R124,R125,R126,R127,    |

|            |         |R128,R129,R130,R131,    |

|            |         |R132,R133,R134,R135,    |

|            |         |R136,R137,R138,R139,    |

|            |         |R140,R141,R142,R143,    |

|            |         |R144,R147,R148,R149,    |

|            |         |R150,R151,R152,R153,    |

|            |         |R154,R155,R156,R157,    |

|            |         |R158,R159,R160,R161,    |

|            |         |R162,R27,R65,R66,R67,   |

|            |         |R68,R69,R70,R71,R72,R73,|

|            |         |R74,R75,R76,R77,R78,R79,|

|            |         |R80,R81,R82,R83,R84,R85,|

|            |         |R86,R87,R88,R89,R90,R91,|

|            |         |R92,R93,R94,R95,R96,R97,|

|            |         |R98,R99                 |

|            |         |                        |

2|RSMT        |3k6      |R11,R17                 |Farago

|R0805       |         |                        |

|            |         |                        |

5|RSMT        |4k7      |R12,R18,R19,R23,R26     |Farago

|R0805       |         |                        |

|            |         |                        |

1|RSMT        |N/A      |R13                     |N/A

|R0805       |         |                        |

|            |         |                        |

10|RSMT        |82       |R145,R146,R29,R31,R33,  |In stock

|R0402       |         |R35,R54,R56,R60,R61     |

|            |         |                        |

4|RSMT        |100      |R15,R2,R21,R9           |Farago

|R0805       |         |                        |

|            |         |                        |

1|RSMT        |22       |R163                    |Farago

|R0805       |         |                        |

|            |         |                        |

10|RSMT        |130      |R164,R165,R28,R30,R32,  |Mouser

|R0402       |         |R34,R55,R57,R58,R59     |

|            |         |                        |

23|RSMT        |4k7      |R166,R167,R168,R169,    |Farago

|R0603       |         |R170,R171,R172,R177,    |

|            |         |R180,R38,R39,R40,R41,   |

|            |         |R42,R43,R44,R45,R46,R47,|

|            |         |R48,R49,R50,R51         |

|            |         |                        |

3|RSMT        |100      |R173,R174,R179          |Farago

|R0603       |         |                        |

|            |         |                        |

6|RSMT        |1k       |R175,R176,R181,R182,    |Farago

|R0603       |         |R183,R184               |

|            |         |                        |

1|RSMT        |330      |R178                    |Farago

|R0603       |         |                        |

|            |         |                        |

3|RSMT        |1k5      |R20,R24,R8              |Farago

|R0805       |         |                        |

|            |         |                        |

1|RSMT        |1k2      |R22                     |Farago

|R0805       |         |                        |

|            |         |                        |

1|RSMT        |6k8      |R25                     |Farago

|R0805       |         |                        |

|            |         |                        |

1|RSMT        |470      |R3                      |Farago

|R0805       |         |                        |

|            |         |                        |

6|RSMT        |1k       |R36,R37,R52,R53,R62,R63 |Farago

|R0805       |         |                        |

|            |         |                        |

1|RSMT        |5k6      |R4                      |Farago

|R0805       |         |                        |

|            |         |                        |

1|RSMT        |22k      |R5                      |Farago

|R0805       |         |                        |

|            |         |                        |

1|RSMT        |10k      |R6                      |Farago

|R0805       |         |                        |

|            |         |                        |

1|RSMT        |33       |R64                     |Farago

|R0805       |         |                        |

|            |         |                        |

1|RSMT        |220k     |R7                      |Farago

|R0805       |         |                        |

|            |         |                        |

2|SFP         |         |P1,P2                   |In stock

|SFP         |         |                        |

|            |         |                        |

4|TPS74401    |         |U1,U3,U5,U7             |Mouser

|QFN20       |         |                        |

|            |         |                        |

1|XCF32P-VOG48|         |U11                     |NuHorizons

|VO48        |         |                        |

|            |         |                        |

1|XV5-FF1136  |         |U9/10                   |NuHorizons

|FF1136      |         |                        |

|            |         |                        |

1|MT4HTF3264HY|         |                        |NuHorizons

|256M DDR2   |         |                        |

|            |         |                        |

|            |         |                        |

## B.2 Component Locations

Fiducial points can be used as main navigation points.
FP5-FP8 located on top layer, since FP1-FP4 are on the bottom.

X coordinates spans accross the board in the range of 750 mils to 7320 mils.
Y coordinates spans accross the board in the range of 1200mils to 5075mils.
FP1-FP4 located on top layer, since FP4-FP8 are on the bottom.

### B2.1 Coordinate system onboard - TOP

### B2.2 Coordinate system onboard - BOTTOM

### B2.3 Table of component locations

Refdes  Location      Pattern  Value

----------------------------------------

FP1     01500 01500   FIDPT

FP2     06900 01700   FIDPT

FP3     06000 04000   FIDPT

FP4     01820 04000   FIDPT

FP5     01820 04000   FIDPT

FP6     01860 02005   FIDPT

FP7     06900 01695   FIDPT

FP8     06855 04460   FIDPT

C1      02810 03945   C0603    10U

C2      07125 02725   C0603    10U

C3      02750 03910   C0603    100N

C4      02810 03785   C0603    100N

C5      06780 02950   C0603    10U

C6      04725 02415   C0603    10U

C7      02530 03904   C0603    10U

C8      07130 02250   E7343    220U

C9      02600 03705   C0603    1N

C10     06625 03150   E7343    1000U

C11     05028 02626   E7343    1000U

C12     03120 01390   C0603    10U

C13     07125 04525   C0603    10U

C14     03060 01355   C0603    100N

C15     03120 01230   C0603    100N

C16     07125 04050   E7343    220U

C17     06780 04750   C0603    10U

C18     04230 04066   C0603    10U

C19     02840 01349   C0603    10U

C20     02910 01150   C0603    1N

C21     06625 04950   E7343    1000U

C22     04505 01510   C0603    10U

C23     07125 01835   C0603    10U

C24     04445 01470   C0603    100N

C25     04505 01350   C0603    100N

C26     06780 02050   C0603    10U

C27     03984 02099   C0603    10U

C28     04225 01464   C0603    10U

C29     07125 01350   E7343    220U

C30     04285 01265   C0603    1N

C31     06625 02250   E7343    1000U

C32     05030 01900   E7343    1000U

C33     05010 01270   C0603    10U

C34     07125 03610   C0603    10U

C35     05045 01330   C0603    100N

C36     05170 01270   C0603    100N

C37     06780 03850   C0603    10U

C38     03556 02147   C0603    10U

C39     05051 01550   C0603    10U

C40     07125 03155   E7343    220U

C41     05250 01480   C0603    1N

C42     06625 04050   E7343    1000U

C43     04221 01841   C0402    47N

C44     04259 01841   C0402    47N

C45     04378 01841   C0402    47N

C46     04338 01847   C0402    47N

C47     04299 01847   C0402    47N

C48     03944 01805   C0402    47N

C49     03165 01160   C0402    47N

C50     03967 01942   C0402    47N

C51     03747 01881   C0402    47N

C52     03210 01160   C0402    47N

C53     03905 01841   C0402    47N

C54     03320 01155   C0402    47N

C55     04417 01807   C0402    47N

C56     03827 01881   C0402    47N

C57     03365 01155   C0402    47N

C58     03866 01841   C0402    47N

C59     03465 01155   C0402    47N

C60     03984 01841   C0402    47N

C61     03510 01155   C0402    47N

C62     04024 01841   C0402    47N

C63     03600 01155   C0402    47N

C64     04142 01841   C0402    47N

C65     03708 01841   C0402    47N

C66     03645 01155   C0402    47N

C67     04063 01845   C0402    47N

C68     03731 01155   C0402    47N

C69     04102 01845   C0402    47N

C70     03472 01797   C0402    47N

C71     03775 01155   C0402    47N

C72     03511 01841   C0402    47N

C73     03630 01841   C0402    47N

C74     04182 01841   C0402    47N

C75     03590 01806   C0402    47N

C76     03590 01919   C0402    47N

C77     03669 01841   C0402    47N

C78     02915 02045   C0402    47N

C79     02915 02000   C0402    47N

C80     02915 01625   C0402    47N

C81     02915 01670   C0402    47N

C82     02320 02475   C0402    47N

C83     02380 02480   C0603    470P

C84     02320 02435   C0402    47N

C85     02380 02425   C0603    470P

C86     02240 02835   A3216    10U

C87     03353 01881   C0402    47N

C88     03253 01745   C0402    47N

C89     03324 01817   C0402    47N

C90     03472 01881   C0402    47N

C91     03433 01920   C0402    47N

C92     03380 01675   C0402    47N

C94     04125 02853   C0402    47N

C95     03807 03075   C0402    47N

C96     03866 02826   C0402    47N

C97     03573 02809   C0402    47N

C98     03453 02887   C0402    47N

C99     02240 01940   A3216    10U

C100    02320 01525   C0402    47N

C101    02380 01525   C0603    470P

C102    02320 01565   C0402    47N

C103    02380 01580   C0603    470P

C104    05170 01925   C0402    47N

C105    05170 01970   C0402    47N

C107    04417 02966   C0402    47N

C108    04417 02831   C0402    47N

C109    04496 02966   C0402    47N

C110    04555 02889   C0402    47N

C111    05335 02745   C0402    47N

C112    05380 01655   C0402    47N

C113    05525 01650   C0603    470P

C114    05765 01440   C0603    470P

C115    05910 01450   C0402    47N

C116    05310 01650   A3216    10U

C117    05980 01480   A3216    10U

C118    04456 01807   C0402    47N

C119    04496 01807   C0402    47N

C120    04565 01895   C0402    47N

C121    04417 01880   C0402    47N

C122    04456 01925   C0402    47N

C123    05420 01785   C0402    47N

C124    04535 01807   C0402    47N

C125    05420 01825   C0402    47N

C126    05695 01795   C0402    47N

C127    05655 01625   C0402    47N

C128    03855 03264   A3216    10U

C129    03185 02715   A3216    10U

C130    04680 03865   C0402    47N

C131    04695 02755   C0402    47N

C132    03076 03649   C0603    100N

C133    04680 03810   C0402    47N

C134    03160 02775   C0402    47N

C135    03669 02870   C0402    47N

C136    04130 03865   C0402    47N

C137    03295 02734   C0603    100N

C138    04299 02831   C0402    47N

C139    04130 03810   C0402    47N

C140    04010 03865   A3216    10U

C141    05760 03575   C0603    100N

C142    03945 02461   C0603    10U

C143    04220 02392   C0402    47N

C144    04141 02392   C0402    47N

C145    04063 02392   C0402    47N

C146    03922 02336   C0402    47N

C147    03922 02257   C0402    47N

C148    03922 02178   C0402    47N

C149    03922 02533   C0402    47N

C150    03922 02611   C0402    47N

C151    03967 02572   C0402    47N

C152    03827 02437   C0402    47N

C153    03748 02437   C0402    47N

C154    03708 02392   C0402    47N

C155    02720 01085   C0603    100N

C156    04690 01285   C0603    100N

C157    03865 02772   C0603    10U

C158    06129 02695   C0402    47N

C159    06127 02955   C0402    47N

C160    04449 04071   C0402    47N

C161    04614 04025   C0402    47N

C162    04625 03652   C0402    47N

C163    04177 03604   C0402    47N

C164    04160 04027   C0402    47N

C165    03787 02668   C0402    47N

C166    04063 02668   C0402    47N

C167    03669 02160   C0402    47N

C168    04139 02114   C0402    47N

C169    03342 02491   C0603    10U

C170    03354 02752   C0402    47N

C171    03337 02356   C0402    47N

C172    03708 02043   C0402    47N

C173    04102 02044   C0402    47N

C174    03922 01982   C0402    47N

C175    04299 01998   C0402    47N

C176    04496 02161   C0402    47N

C177    04558 02375   C0402    47N

C178    04479 02612   C0402    47N

C179    04181 02628   C0402    47N

C180    06128 02572   C0402    47N

C181    06127 02900   C0402    47N

C182    05290 02790   C0402    47N

C183    04680 03125   C0402    47N

C184    04427 03247   C0402    47N

C185    03188 03131   C0402    47N

D1      00980 02945   D2LED100 3MM

D2      00980 02045   D2LED100 3MM

D3      00980 04105   D2LED100 3MM

J1      03000 01000   PCIEX4M

J2      02657 01220   PIN2

J3      03090 03675   SODIM200

J4      06136 02207   PIN2

J5      00935 04885   FEACON

J6      02760 03000   PIN2

J7      06130 01300   JTAGCON

L1      04055 01605   L0603    220

L2      04305 01605   L0603    220

L3      04360 01605   L0603    220

L4      04250 01605   L0603    220

L5      04415 01605   L0603    220

L6      03935 01605   L0603    220

L7      03780 01605   L0603    220

L8      03904 01616   L0603    220

L9      03865 01605   L0603    220

L10     04086 01637   L0603    220

L11     04138 01605   L0603    220

L12     04030 01615   L0603    220

L13     04195 01605   L0603    220

L14     03480 01605   L0603    220

L15     03535 01605   L0603    220

L16     03640 01640   L0603    220

L17     03590 01605   L0603    220

L18     02345 02370   L0603    220

L19     02345 02535   L0603    220

L20     03185 01930   L0603    220

L21     03205 01770   L0603    220

L22     03370 01625   L0603    220

L23     03425 01605   L0603    220

L28     02345 01470   L0603    220

L29     02345 01635   L0603    220

L34     05220 01740   L0603    220

L35     05980 01660   L0603    220

L36     04470 01605   L0603    220

L37     04755 01870   L0603    220

L38     04755 01784   L0603    220

L39     04700 01800   L0603    220

M1      00720 03490   SCJUMPER

P1      02230 02725   SFP

P2      02230 01825   SFP

P3      05445 01720   SFF2X5PIG

R1      06260 02595   R0805    0

R2      06260 02935   R0805    100

R3      02470 03825   R0805    470

R4      02685 03655   R0805    5K6

R5      06520 02795   R0805    22K

R6      02685 03755   R0805    10K

R7      06620 02795   R0805    220K

R8      06260 04395   R0805    1K5

R9      06260 04730   R0805    100

R10     02780 01270   R0805    1K8

R11     02995 01200   R0805    3K6

R12     06520 04595   R0805    4K7

R13     06620 04595   R0805    N/A

R14     06260 01690   R0805    0

R15     06260 02035   R0805    100

R16     04165 01385   R0805    1K8

R17     04375 01300   R0805    3K6

R18     06520 01895   R0805    4K7

R19     06620 01895   R0805    4K7

R20     06260 03500   R0805    1K5

R21     06260 03835   R0805    100

R22     05151 01612   R0805    1K2

R23     05200 01395   R0805    4K7

R24     06520 03695   R0805    1K5

R25     06620 03695   R0805    6K8

R26     06135 02325   R0805    4K7

R27     03944 01841   R0402    51

R28     02770 02080   R0402    130

R29     02815 02120   R0402    82

R30     02770 02000   R0402    130

R31     02815 02040   R0402    82

R32     02815 01550   R0402    130

R33     02770 01590   R0402    82

R34     02815 01630   R0402    130

R35     02770 01670   R0402    82

R36     01400 02960   R0805    1K

R37     01400 02850   R0805    1K

R38     01985 02280   R0603    4K7

R39     01985 02335   R0603    4K7

R40     01985 02390   R0603    4K7

R41     01985 02445   R0603    4K7

R42     01985 02500   R0603    4K7

R43     01985 02555   R0603    4K7

R44     01985 02610   R0603    4K7

R45     01985 01380   R0603    4K7

R46     01985 01435   R0603    4K7

R47     01985 01490   R0603    4K7

R48     01985 01545   R0603    4K7

R49     01985 01600   R0603    4K7

R50     01985 01655   R0603    4K7

R51     01985 01710   R0603    4K7

R52     01400 02060   R0805    1K

R53     01400 01950   R0805    1K

R54     05300 01900   R0402    82

R55     05345 01860   R0402    130

R56     05300 01950   R0402    82

R57     05345 02005   R0402    130

R58     05775 01705   R0402    130

R59     05775 01670   R0402    130

R60     05735 01705   R0402    82

R61     05735 01670   R0402    82

R62     01400 04010   R0805    1K

R63     01400 04120   R0805    1K

R64     02810 03630   R0805    33

R65     03110 02920   R0402    51

R66     03155 02815   R0402    51

R67     03230 02920   R0402    51

R68     03185 02815   R0402    51

R69     03110 02960   R0402    51

R70     03230 02960   R0402    51

R71     03155 02855   R0402    51

R72     03240 03250   R0402    51

R73     03185 02855   R0402    51

R74     03240 03130   R0402    51

R75     03170 03015   R0402    51

R76     03185 03000   R0402    51

R77     03300 03205   R0402    51

R78     03300 03130   R0402    51

R79     03340 03205   R0402    51

R80     03340 03130   R0402    51

R81     03380 03175   R0402    51

R82     03380 03250   R0402    51

R83     03420 03175   R0402    51

R84     03420 03250   R0402    51

R85     03750 03250   R0402    51

R86     03750 03175   R0402    51

R87     04338 03067   R0402    51

R88     04599 03138   R0402    51

R89     03485 03175   R0402    51

R90     03485 03250   R0402    51

R91     03525 03175   R0402    51

R92     03525 03250   R0402    51

R93     03565 03175   R0402    51

R94     03565 03250   R0402    51

R95     03605 03175   R0402    51

R96     03607 03250   R0402    51

R97     03670 03175   R0402    51

R98     03670 03250   R0402    51

R99     03710 03175   R0402    51

R100    03710 03250   R0402    51

R101    04180 03910   R0402    51

R102    04180 03810   R0402    51

R103    04220 03910   R0402    51

R104    04220 03810   R0402    51

R105    04260 03910   R0402    51

R106    04260 03810   R0402    51

R107    04300 03910   R0402    51

R108    04300 03810   R0402    51

R109    04340 03910   R0402    51

R110    04340 03810   R0402    51

R111    04380 03910   R0402    51

R112    04380 03810   R0402    51

R113    04420 03910   R0402    51

R114    04420 03810   R0402    51

R115    04460 03910   R0402    51

R116    04460 03810   R0402    51

R117    04500 03910   R0402    51

R118    04500 03810   R0402    51

R119    04540 03910   R0402    51

R120    04540 03810   R0402    51

R121    04580 03910   R0402    51

R122    04580 03810   R0402    51

R123    04620 03810   R0402    51

R124    04620 03910   R0402    51

R125    04042 03215   R0402    51

R126    04045 03125   R0402    51

R127    04005 03170   R0402    51

R128    04085 03125   R0402    51

R129    04165 03245   R0402    51

R130    04125 03170   R0402    51

R131    04205 03245   R0402    51

R132    04165 03170   R0402    51

R133    04305 03240   R0402    51

R134    04205 03170   R0402    51

R135    04305 03190   R0402    51

R136    04245 03170   R0402    51

R137    04485 03256   R0402    51

R138    04427 03158   R0402    51

R139    04485 03218   R0402    51

R140    04467 03158   R0402    51

R141    04730 03085   R0402    51

R142    04655 03085   R0402    51

R143    04730 03045   R0402    51

R144    04655 03045   R0402    51

R145    02770 02590   R0402    82

R146    02770 02670   R0402    82

R147    04730 02980   R0402    51

R148    04655 02980   R0402    51

R149    04730 02940   R0402    51

R150    04655 02940   R0402    51

R151    03764 02809   R0402    51

R152    03827 02910   R0402    51

R153    04220 02828   R0402    51

R154    04599 03177   R0402    51

R155    04730 02900   R0402    51

R156    04655 02900   R0402    51

R157    04730 02860   R0402    51

R158    04655 02860   R0402    51

R159    04730 02795   R0402    51

R160    04730 02755   R0402    51

R161    04655 02755   R0402    51

R162    04655 02795   R0402    51

R163    04759 02627   R0805    22

R164    02815 02630   R0402    130

R165    02815 02550   R0402    130

R166    04153 03586   R0603    4K7

R167    04162 04112   R0603    4K7

R168    04567 04110   R0603    4K7

R169    04626 03569   R0603    4K7

R170    05560 03575   R0603    4K7

R171    05580 03755   R0603    4K7

R172    06203 02930   R0603    4K7

R173    06203 02803   R0603    100

R174    06205 02745   R0603    100

R175    03539 02747   R0603    1K

R176    03735 02747   R0603    1K

R177    06045 02845   R0603    4K7

R178    06045 02750   R0603    330

R179    03595 02690   R0603    100

R180    02545 03080   R0603    4K7

R181    03135 01985   R0603    1K

R182    03135 02100   R0603    1K

R183    04755 02080   R0603    1K

R184    04755 02135   R0603    1K

RN1     01695 02985   RN1206X  22

RN2     01860 03145   RN1206X  22

RN3     01885 02985   RN1206X  22

RN4     02110 03145   RN1206X  22

RN5     02160 02985   RN1206X  22

RN6     02425 02985   RN1206X  22

RN7     02375 03145   RN1206X  22

RN8     02575 02985   RN1206X  22

U1      02645 03870   QFN20

U2      07125 02450   DIP-EBS

U3      02955 01315   QFN20

U4      07125 04250   DIP-EBS

U5      04340 01430   QFN20

U6      07125 01550   DIP-EBS

U7      05085 01435   QFN20

U8      07125 03350   DIP-EBS

U9      03945 01765   FF1136

U10     03295 01765   FF1136

U11     06105 03015   VO48

X1      02645 02225   XO5X7    125.00MHZ

X2      02645 01780   XO5X7    155.52MHZ

X3      05175 02090   XO5X7    155.52MHZ

X4      02645 02775   XO5X7    200.00MHZ

### B2.4 Insertion diagram TOP

### B2.5 Insertion diagram BOTTOM

# Apendix C. User Constraints File

#- R2E3FFFF.UCF

#- ============

#-

#- (C) Gyorgy Horvath, DTMIT-BUTE, 2002..2008

#- Cores for GPLANAR3 hardware, V5 FPGA on-board

#-

#- R2E3FFxx cores contains RESIDENTAL MFG/TEST cores for

#- XC5VLX50T-1FF1136C OR XC5VLX110T-1FF1136C Virtex-5 devices.

#-

#- The following block's pinout are constrained here:

#-

#- 1. PCI Expressx4 - designated as J1 (gold plated edge connector)

#- 2. Dual SFP MrMs - designated as P1 and P2

#- 3. GPON ONT OSA  - designated as P3 (NU-73B94B-P Optoway device)

#- 4. DDR2 RAM/SO-DIMM - J3 on-board

#- 5. Feature connector - 40 pin IDE compatible BERG type at J5

#- 6. Reference clocks

#-

#- Created:  10 mar 2008   - G.H. Written

#- Modified: 10 mar 2008   - G.H. First approach

#-

#-

CONFIG PART = XC5VLX50T-FF1136-1 ;

#-

#-

###############################################################################

#- 1. PCI Expressx4 - designated as J1 (gold plated edge connector)

###############################################################################

#

# - Bus reset from PCI Express host initiates PROG on the FPGA (J4 closed)

#   Optionally it can be routed to IDE-RST - J4/2 to J5/1. Here is the LOC:

NET "sys_reset_n"      LOC = "H14"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;  # PXPERST~

#

# -Transceiver instance placement.

#   -PCIe Lanes 0, 1

INST "ep/BU2/U0/pcie_ep0/pcie_blk/pcie_gt_wrapper_i/GTPD[0].GTP_i" LOC = GTP_DUAL_X0Y3;

#   -PCIe Lanes 2, 3

INST "ep/BU2/U0/pcie_ep0/pcie_blk/pcie_gt_wrapper_i/GTPD[2].GTP_i" LOC = GTP_DUAL_X0Y2;

# -Global clock input spec.

NET "ep/BU2/U0/pcie_ep0/pcie_blk/pcie_gt_wrapper_i/gt_refclk_out[0]" TNM_NET = "MGTCLK" ;

TIMESPEC "TS_MGTCLK"  = PERIOD "MGTCLK" 100.00 MHz HIGH 50 % ;

#-

#-

###############################################################################

#- 2. Dual SFP MrMs - designated as P1 and P2

###############################################################################

#= P1 - SFP receptacle ========================================================

NET "TXFAULT[0]"       LOC = "E13"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "TXDIS[0]"         LOC = "G12"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "SDO[0]"           LOC = "E12"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "SCLK[0]"          LOC = "D12"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "PLUG_N[0]"        LOC = "C13"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "RATS[0]"          LOC = "A13"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "LOS[0]"           LOC = "B13"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "LEDACT_N[0]"      LOC = "G11"  | IOSTANDARD = LVCMOS33          | NODELAY ;

NET "LEDLOS_N[0]"      LOC = "F11"  | IOSTANDARD = LVCMOS33          | NODELAY ;

#-GTP_DUAL_X0Y5

NET  "TXP[0]"          LOC = "B4"  ; # TX Polarity has to be inverted here

NET  "TXN[0]"          LOC = "B3"  ;

NET  "RXP[0]"          LOC = "A3"  ;

NET  "RXN[0]"          LOC = "A2"  ;

#= P2 - SFP receptacle ========================================================

NET "TXFAULT[1]"       LOC = "D11"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "TXDIS[1]"         LOC = "E11"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "SDO[1]"           LOC = "D10"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "SCLK[1]"          LOC = "E9"   | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "PLUG_N[1]"        LOC = "F9"   | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "RATS[1]"          LOC = "E8"   | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "LOS[1]"           LOC = "F8"   | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "LEDACT_N[1]"      LOC = "C12"  | IOSTANDARD = LVCMOS33          | NODELAY ;

NET "LEDLOS_N[1]"      LOC = "B12"  | IOSTANDARD = LVCMOS33          | NODELAY ;

#-GTP_DUAL_X0Y5

NET  "TXP[1]"          LOC = "E2"  ;

NET  "TXN[1]"          LOC = "D2"  ;

NET  "RXP[1]"          LOC = "D1"  ; # RX Polarity has to be inverted here

NET  "RXN[1]"          LOC = "C1"  ;

#-

#-

###############################################################################

#- 3. GPON ONT OSA  - designated as P3 (NU-73B94B-P Optoway device)

###############################################################################

NET "LEDACT_N[2]"      LOC = "F13"  | IOSTANDARD = LVCMOS33          | NODELAY ;

NET "LEDLOS_N[2]"      LOC = "G13"  | IOSTANDARD = LVCMOS33          | NODELAY ;

NET "BEN3"             LOC = "AN14" | IOSTANDARD = LVCMOS33          | NODELAY ;

NET "SD3"              LOC = "AP14" | IOSTANDARD = LVCMOS33          | NODELAY ;

#-GTP_DUAL_X0Y0

NET  "TD3P"            LOC = "AN4" ; # TX Polarity has to be inverted here

NET  "TD3N"            LOC = "AN3" ;

NET  "RD3P"            LOC = "AP3" ; # RX Polarity has to be inverted here

NET  "RD3N"            LOC = "AP2" ;

#-

#-

###############################################################################

#- 4. DDR2 RAM/SO-DIMM - J3 on-board

###############################################################################

#- I/O standards

NET  "ddr2_dq[*]"      IOSTANDARD = SSTL18_II_DCI;

NET  "ddr2_a[*]"       IOSTANDARD = SSTL18_I;

NET  "ddr2_ba[*]"      IOSTANDARD = SSTL18_I;

NET  "ddr2_ras_n"      IOSTANDARD = SSTL18_I;

NET  "ddr2_cas_n"      IOSTANDARD = SSTL18_I;

NET  "ddr2_we_n"       IOSTANDARD = SSTL18_I;

NET  "ddr2_cs_n[*]"    IOSTANDARD = SSTL18_I;

NET  "ddr2_odt[*]"     IOSTANDARD = SSTL18_I;

NET  "ddr2_cke[*]"     IOSTANDARD = SSTL18_I;

NET  "ddr2_reset_n"    IOSTANDARD = LVCMOS33;

NET  "ddr2_dm[*]"      IOSTANDARD = SSTL18_II_DCI;

NET  "GCLKP"           IOSTANDARD = LVPECL_25;

NET  "GCLKN"           IOSTANDARD = LVPECL_25;

NET  "sys_rst_n"       IOSTANDARD = LVCMOS33 | PULLUP;

NET  "phy_init_done"   IOSTANDARD = LVCMOS33;

NET  "ddr2_dqs[*]"     IOSTANDARD = DIFF_SSTL18_II_DCI;

NET  "ddr2_dqs_n[*]"   IOSTANDARD = DIFF_SSTL18_II_DCI;

NET  "ddr2_ck[*]"      IOSTANDARD = DIFF_SSTL18_II;

NET  "ddr2_ck_n[*]"    IOSTANDARD = DIFF_SSTL18_II;

#- DDR2 Module SPD (Serial Prom Data) IF pinout

NET "DRSDA"            LOC = "AH19" | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "DRSCL"            LOC = "AF19" | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

#- Pinouts for control signals

NET  "sys_rst_n"       LOC = "J22" ;	 # J5/20 (BFKEY) on the Fea. Conn. for testing

NET  "phy_init_done"   LOC = "J16" ;	 # J5/21 (BFDRQ) on the Fea. Conn. for testing

NET  "ddr2_reset_n"    LOC = "K19" ;	 # J5/39 (BFACT) on the Fea. Conn. for testing

NET  "ddr2_ras_n"      LOC = "AA31" ;	     #Bank 17

NET  "ddr2_cas_n"      LOC = "Y29" ;	      #Bank 17

NET  "ddr2_we_n"       LOC = "V28" ;	      #Bank 17

NET  "ddr2_cs_n[0]"    LOC = "Y31" ;	      #Bank 17

NET  "ddr2_cs_n[1]"    LOC = "AA29" ;	     #Bank 17 !!!!!

NET  "ddr2_odt[0]"     LOC = "T34" ;	      #Bank 11

NET  "ddr2_odt[1]"     LOC = "V30" ;	      #Bank 17 !!!!!

NET  "ddr2_cke[0]"     LOC = "N32" ;	      #Bank 11

NET  "ddr2_cke[1]"     LOC = "M32" ;	      #Bank 11 !!!!!

NET  "ddr2_ck[0]"      LOC = "B32" ;	      #Bank 11

NET  "ddr2_ck_n[0]"    LOC = "A33" ;	      #Bank 11

NET  "ddr2_ck[1]"      LOC = "AN34" ;	     #Bank 13

NET  "ddr2_ck_n[1]"    LOC = "AN33" ;	     #Bank 13

#- Address

NET  "ddr2_ba[0]"      LOC = "V27" ;	      #Bank 17

NET  "ddr2_ba[1]"      LOC = "W31" ;	      #Bank 17

NET  "ddr2_ba[2]"      LOC = "P32" ;	      #Bank 11 !!!!!

NET  "ddr2_a[0]"       LOC = "AA30" ;      #Bank 17

NET  "ddr2_a[1]"       LOC = "V24" ;	      #Bank 17

NET  "ddr2_a[2]"       LOC = "V29" ;	      #Bank 17

NET  "ddr2_a[3]"       LOC = "R34" ;	      #Bank 11

NET  "ddr2_a[4]"       LOC = "Y28" ;	      #Bank 17

NET  "ddr2_a[5]"       LOC = "W29" ;	      #Bank 17

NET  "ddr2_a[6]"       LOC = "U33" ;	      #Bank 11

NET  "ddr2_a[7]"       LOC = "U32" ;	      #Bank 11

NET  "ddr2_a[8]"       LOC = "V25" ;	      #Bank 17

NET  "ddr2_a[9]"       LOC = "P34" ;	      #Bank 11

NET  "ddr2_a[10]"      LOC = "W26" ;	      #Bank 17

NET  "ddr2_a[11]"      LOC = "T33" ;	      #Bank 11

NET  "ddr2_a[12]"      LOC = "U31" ;	      #Bank 11

NET  "ddr2_a[13]"      LOC = "AB31" ;      #Bank 17

NET  "ddr2_a[14]"      LOC = "R33" ;	      #Bank 11 !!!!!

NET  "ddr2_a[15]"      LOC = "R32" ;	      #Bank 11 !!!!!

#- Lane 0

NET  "ddr2_dq[0]"      LOC = "L29" ;	      #Bank 15

NET  "ddr2_dq[1]"      LOC = "J29" ;	      #Bank 15

NET  "ddr2_dq[2]"      LOC = "P29" ;	      #Bank 15

NET  "ddr2_dq[3]"      LOC = "P30" ;	      #Bank 15

NET  "ddr2_dq[4]"      LOC = "H29" ;	      #Bank 15

NET  "ddr2_dq[5]"      LOC = "G30" ;	      #Bank 15

NET  "ddr2_dq[6]"      LOC = "F30" ;	      #Bank 15

NET  "ddr2_dq[7]"      LOC = "G31" ;	      #Bank 15

NET  "ddr2_dqs[0]"     LOC = "E29" ;	      #Bank 15

NET  "ddr2_dqs_n[0]"   LOC = "F29" ;	      #Bank 15

NET  "ddr2_dm[0]"      LOC = "H30" ;	      #Bank 15

#- Lane 1

NET  "ddr2_dq[8]"      LOC = "F31" ;	      #Bank 15

NET  "ddr2_dq[9]"      LOC = "E31" ;	      #Bank 15

NET  "ddr2_dq[10]"     LOC = "P31" ;	      #Bank 15

NET  "ddr2_dq[11]"     LOC = "R31" ;	      #Bank 15

NET  "ddr2_dq[12]"     LOC = "L30" ;	      #Bank 15

NET  "ddr2_dq[13]"     LOC = "K31" ;	      #Bank 15

NET  "ddr2_dq[14]"     LOC = "M30" ;	      #Bank 15

NET  "ddr2_dq[15]"     LOC = "N29" ;	      #Bank 15

NET  "ddr2_dqs[1]"     LOC = "M31" ;	      #Bank 15

NET  "ddr2_dqs_n[1]"   LOC = "N30" ;	      #Bank 15

NET  "ddr2_dm[1]"      LOC = "J31" ;	      #Bank 15

#- Lane 2

NET  "ddr2_dq[16]"     LOC = "B33" ;	      #Bank 11

NET  "ddr2_dq[17]"     LOC = "C33" ;	      #Bank 11

NET  "ddr2_dq[18]"     LOC = "F34" ;	      #Bank 11

NET  "ddr2_dq[19]"     LOC = "E32" ;	      #Bank 11

NET  "ddr2_dq[20]"     LOC = "C34" ;	      #Bank 11

NET  "ddr2_dq[21]"     LOC = "D34" ;	      #Bank 11

NET  "ddr2_dq[22]"     LOC = "C32" ;	      #Bank 11

NET  "ddr2_dq[23]"     LOC = "D32" ;	      #Bank 11

NET  "ddr2_dqs[2]"     LOC = "F33" ;	      #Bank 11

NET  "ddr2_dqs_n[2]"   LOC = "E34" ;	      #Bank 11

NET  "ddr2_dm[2]"      LOC = "E33" ;	      #Bank 11

#- Lane 3

NET  "ddr2_dq[24]"     LOC = "H34" ;	      #Bank 11

NET  "ddr2_dq[25]"     LOC = "H33" ;	      #Bank 11

NET  "ddr2_dq[26]"     LOC = "K32" ;	      #Bank 11

NET  "ddr2_dq[27]"     LOC = "L33" ;	      #Bank 11

NET  "ddr2_dq[28]"     LOC = "G33" ;	      #Bank 11

NET  "ddr2_dq[29]"     LOC = "G32" ;	      #Bank 11

NET  "ddr2_dq[30]"     LOC = "J32" ;	      #Bank 11

NET  "ddr2_dq[31]"     LOC = "K33" ;	      #Bank 11

NET  "ddr2_dqs[3]"     LOC = "L34" ;	      #Bank 11

NET  "ddr2_dqs_n[3]"   LOC = "K34" ;	      #Bank 11

NET  "ddr2_dm[3]"      LOC = "J34" ;	      #Bank 11

#- Lane 4

NET  "ddr2_dq[32]"     LOC = "V32" ;	     #Bank 13

NET  "ddr2_dq[33]"     LOC = "V33" ;	     #Bank 13

NET  "ddr2_dq[34]"     LOC = "AA33" ;	    #Bank 13

NET  "ddr2_dq[35]"     LOC = "AB33" ;	    #Bank 13

NET  "ddr2_dq[36]"     LOC = "Y33" ;	     #Bank 13

NET  "ddr2_dq[37]"     LOC = "Y32" ;	     #Bank 13

NET  "ddr2_dq[38]"     LOC = "Y34" ;	     #Bank 13

NET  "ddr2_dq[39]"     LOC = "AA34" ;	    #Bank 13

NET  "ddr2_dqs[4]"     LOC = "W34" ;	     #Bank 13

NET  "ddr2_dqs_n[4]"   LOC = "V34" ;	     #Bank 13

NET  "ddr2_dm[4]"      LOC = "AB32" ;	    #Bank 13

#- Lane 5

NET  "ddr2_dq[40]"     LOC = "AC32" ;	    #Bank 13

NET  "ddr2_dq[41]"     LOC = "Ac33" ;	    #Bank 13

NET  "ddr2_dq[42]"     LOC = "AE32" ;	    #Bank 13

NET  "ddr2_dq[43]"     LOC = "AE34" ;	    #Bank 13

NET  "ddr2_dq[44]"     LOC = "AD32" ;	    #Bank 13

NET  "ddr2_dq[45]"     LOC = "AK32" ;	    #Bank 13

NET  "ddr2_dq[46]"     LOC = "AF33" ;	    #Bank 13

NET  "ddr2_dq[47]"     LOC = "AF34" ;	    #Bank 13

NET  "ddr2_dqs[5]"     LOC = "AC34" ;	    #Bank 13

NET  "ddr2_dqs_n[5]"   LOC = "AD34" ;	    #Bank 13

NET  "ddr2_dm[5]"      LOC = "AE33" ;	    #Bank 13

#- Lane 6

NET  "ddr2_dq[48]"     LOC = "AH34" ;	    #Bank 13

NET  "ddr2_dq[49]"     LOC = "AJ34" ;	    #Bank 13

NET  "ddr2_dq[50]"     LOC = "AK33" ;	    #Bank 13

NET  "ddr2_dq[51]"     LOC = "AJ32" ;	    #Bank 13

NET  "ddr2_dq[52]"     LOC = "AM33" ;	    #Bank 13

NET  "ddr2_dq[53]"     LOC = "AK34" ;	    #Bank 13

NET  "ddr2_dq[54]"     LOC = "AP32" ;	    #Bank 13

NET  "ddr2_dq[55]"     LOC = "AM32" ;	    #Bank 13

NET  "ddr2_dqs[6]"     LOC = "AL34" ;	    #Bank 13

NET  "ddr2_dqs_n[6]"   LOC = "AL33" ;	    #Bank 13

NET  "ddr2_dm[6]"      LOC = "AN32" ;	    #Bank 13

#- Lane 7

NET  "ddr2_dq[56]"     LOC = "AF31" ;	    #Bank 17

NET  "ddr2_dq[57]"     LOC = "AG30" ;	    #Bank 17

NET  "ddr2_dq[58]"     LOC = "AD29" ;	    #Bank 17

NET  "ddr2_dq[59]"     LOC = "AE29" ;	    #Bank 17

NET  "ddr2_dq[60]"     LOC = "AK31" ;	    #Bank 17

NET  "ddr2_dq[61]"     LOC = "AD30" ;	    #Bank 17

NET  "ddr2_dq[62]"     LOC = "AH29" ;	    #Bank 17

NET  "ddr2_dq[63]"     LOC = "AF29" ;	    #Bank 17

NET  "ddr2_dqs[7]"     LOC = "AJ30" ;	    #Bank 17

NET  "ddr2_dqs_n[7]"   LOC = "AH30" ;	    #Bank 17

NET  "ddr2_dm[7]"      LOC = "AF30" ;	    #Bank 17

#-

#-

###############################################################################

#- 5. Feature connector - 40 pin IDE compatible BERG type at J5

###############################################################################

#- 16 bits data

NET "FD[0]"            LOC = "G16"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FD[1]"            LOC = "L15"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FD[2]"            LOC = "J15"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FD[3]"            LOC = "H15"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FD[4]"            LOC = "G15"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FD[5]"            LOC = "L14"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FD[6]"            LOC = "K14"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FD[7]"            LOC = "J14"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FD[8]"            LOC = "H20"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FD[9]"            LOC = "J20"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FD[10]"           LOC = "L20"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FD[11]"           LOC = "J21"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FD[12]"           LOC = "K21"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FD[13]"           LOC = "L21"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FD[14]"           LOC = "G22"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FD[15]"           LOC = "H22"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

#- Controls

#NET "FRST"             LOC = "H14"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

#NET "FKEY"             LOC = "J22"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

#NET "FDRQ"             LOC = "J16"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

#NET "FACT"             LOC = "K19"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FIORN"            LOC = "L16"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FIOWN"            LOC = "K16"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FIOCSN"           LOC = "G23"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FBALE"            LOC = "K22"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FA[0]"            LOC = "H19"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FA[1]"            LOC = "K18"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FA[2]"            LOC = "H23"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FCSN[0]"          LOC = "J19"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FCSN[1]"          LOC = "L19"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FIORDY"           LOC = "H17"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "FIRQ"             LOC = "H18"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

#-

###############################################################################

#- 6. Reference clocks

###############################################################################

# - 125.00 MHz GE  Reference for Dual SFPs from X1

NET  "GERCKP"          LOC = "H4"  ;            # Ref.Clock dedicated

NET  "GERCKN"          LOC = "H3"  ;            # at GTP_DUAL_X0Y4

# - 155.56 MHz SDH Reference for Dual SFPs from X2

NET  "OCRCKP"          LOC = "D4"  ;            # Ref.Clock dedicated

NET  "OCRCKN"          LOC = "E4"  ;            # at GTP_DUAL_X0Y5 - SFPs

# - 155.56 MHz SDH Reference for GPON ONT from X3

NET  "PONRCKP"         LOC = "AL4" ;            # Ref.Clock dedicated

NET  "PONRCKN"         LOC = "AL5" ;            # at GTP_DUAL_X0Y0 - GPON

# - 100 MHz PCI Express reference clock from the edge connector

NET  "PXCLKP"          LOC = "P4"  ;            # Ref.Clock dedicated

NET  "PXCLKN"          LOC = "P3"  ;            # at GTP_DUAL_X0Y3 - PCIEXP

# - 200 MHz DDR2 SODIMM reference clock from X4

NET  "GCLKP"           LOC = "K17" ;	           # To global glock

NET  "GCLKN"           LOC = "L18" ;	           # resources

###############################################################################

#- 7. Internal JTAG controller

###############################################################################

NET "ITCK"            LOC = "AG15"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "ITDO"            LOC = "AG16"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "ITDI"            LOC = "AH17"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;

NET "ITMS"            LOC = "AG17"  | IOSTANDARD = LVCMOS33 | PULLUP | NODELAY ;